EXPRESS–METHOD OF VALUATION A TOTAL MICROBIOLOGICAL

POLLUTION OF WATER BY THE FLUORESCENT DNA–SPECIFIC DYES

V.S.Sibirtsev 1   To whom correspondence should be addressed; fax: +7 (812) 327-97-76; e-mail: vsib@b10.vniim.ru, vs1969r@mail.ru;  websyte:  http://www.vs1969r.narod.ru/indexen.htm. and A.V.Garabadzhiu 2

1 Mendeleyev Russian Research Institute for Metrology; Moscowskij pr. 19, St. Petersburg, 190005 Russia

2 St. Petersburg State Technological Institute, Zagorodnyi pr. 49, St. Petersburg, 190013 Russia

Abstracts. New method are described, which can be applied for express valuation of a level microbial pollution of water directly on a place where take sample.

Key words: microbial pollution, fluorescent dyes, DNA.

Microbiological pollution is one of important parameters of quality for a water, food products and etc. The most standard method determination of its is plated of analyzed material on medium with subsequent (after incubation) estimation of number formed microbial colones. The main defects of a given method are: significant time, necessary for analysis fulfilment (from 24 hours and more), as well as difficulty of automation of the analysis process, and accordingly, significant role subjective factor.

As alternative, way of valuation general microbiological pollution a water we are developed, that have, in comparison with a above mentioned standard method, smaller sensitivity, but and requiring considerably smaller time for analysis fulfilment (in limits of several minutes). Besides our method has considerably large opportunity for automation of analysis process, as well as differs by that analysis (at availability portable fluorimeter which are manufactured by a industry) can be executed directly on a places where take sample, without transportation them in stationary laboratory.

The essence of a presented method consists in following. To taken sample add a water solution A, containing:  2M NaCl + 0.1M Na2EDTA (ethylenediaminetetraacetic acid disodium salt) + 0.01M Tris (2-amino-2-hydroxymethyl-1,3-propandiol) +  0.5 vol. %  Triton Х-100 (union detergent) [1] – which enables to support the sample pH in a range 7.8–8.2, as well as destroys of cell membranes for maintenance unobstructed  access of dye to microbial DNA.  Thus the volumetric ratio of initial sample to a solution A should be, about, 10 to 1. Further, sample are incubated during several minutes (at t0=25 0C, up to a establishment of the stable indications on fluorimeter). Then,  the value of Io parameter (fluorescent intensity of  modified sample) are determined at lengths of waves of excitation and emission: 360 and 460 nm, accordingly. Then, to modified sample add a solution of the DAPI

2

(4',6-diamidino-2-phenyl-indole – fluorescent DNA–specific dye) [2,3] and under the same conditions, as earlier, are determined the value of Id parameter.

Then, value:   К = lg[Io/(Id–Io)]

are calculated  and under the formula:  С = 10а0+а1К

(where the factors а0 and а1 find experimentally for a particular fluorimeter type, modes and conditions of measurement) are determined the total quantity of microbes in sample (С).

With use the TKO-100 portable microfluorimeter (manufactured by a firm "Serva", Germany) the given technique has allowed us for various microbes strains (Escherichia coli, Salmonella, Shigella lexneri and other) were determined the total quantity of microbes in sample since 20 cells/ml, with a error not more than 30 %, expending not more than 10 mines on one measurement.

Our method can be used, in particular, for express valuation of a level microbial pollution directly on a place where take sample. Then (if a situation critical or is registered near to those), in stationary laboratory can be conducted the refinement of pollution parameters.

On the other hand, by use, for example, flow citofluorimeter the floor level of microbes detection by our method can be reduced, as a minimum, on the order. However, thus the method сan be applied already only in stationary conditions. Besides our method can be advanced further in the plan of the immobilization the fluorescent dye on a firm surface, use of a agreed complex from several dyes with various properties, application the "internal standard" for reduction of a determination error and etc.

More information on our works in it and other adjacent directions can be on websyte:

http:\\www.vs1969r.narod.ru\indexen.htm.

REFERENCES

1. P. R. COOK: EMBO Journal,  3, 1837 (1984).

2. M. L. BARCELLONA, R. FAVILLA, J. VON BERGER et. all: Archives Biochem. Biophys., 250 (1), 48 (1986).

3. V. S. SIBIRTSEV, A. V. GARABADZHIU, S. D. IVANOV: Russian Journal of Bioorganic Chemistry, 20 (6), 548 (1994).